## Slide 1
Gopal Bhatt1 and Lewis Linker2
1 Penn State, 2 US EPA
09/24/2018
Application of Phase 6 Watershed Model to Climate Change Assessment
STAC Workshop: Climate Change Modeling 2.0
September 24, 2018

## Slide 2
Presentation outline
Estimated impacts of 2025 and 2050 climate change on the watershed delivery of nutrients and sediment.
Decadal series of climate change assessment for the years 2025, 2035, and 2045.
2025
2035
2045
2055
2065
2025
2050
2017 climate change assessment
2019 climate change assessment

## Slide 3
STAC recommendations [1]
[1] Page 8 http://www.chesapeake.org/pubs/360_Johnson2016.pdf
2017 Assessment

## Slide 4
Trend: extrapolation of long-term (88-year) trends
Ensemble: 31-member ensemble of RCP4.5 GCMs
Summary of precipitation and temperature
2017 Assessment
Precipitation (% change) Temperature (°C change)
Years
change is shown in reference to 1995

## Slide 5
extrapolation of trends Δ 90th percentile (P90)
O Ensemble Median (P50) 10th percentile (P10)
Summary of precipitation change
YEAR 2025
YEAR 2050
2017 Assessment
Precipitation Change (percent)

## Slide 6
3.11% increase in average annual rainfall volume
6.28% increase in average annual rainfall volume
YEAR 2025
YEAR 2050
2017 Assessment

## Slide 7
extrapolation of trends Δ 90th percentile (P90)
O Ensemble Median (P50) 10th percentile (P10)
Summary of temperature change
YEAR 2025
YEAR 2050
2017 Assessment
Temperature Change (Celsius)

## Slide 8
1.12°C increase in average annual temperature
2.03°C increase in average annual temperature
YEAR 2025
YEAR 2050
2017 Assessment

## Slide 9
Monthly delta change to hourly events
2017 Assessment
(a) Observed changes in rainfall intensity over the last century (based on Groisman et al. 2004, Figure 10).
(b) Equal distribution
Summary of daily rainfall data
Downscaling monthly change to deciles
Deciles vs. Percent volume (Potter, PA)
About 50% of the rainfall volume lies in top 10% intensity events
Calibration rainfall (inches/day)
Change in daily volume (inches/day)

## Slide 10
Differences in the watershed delivery of flow, nitrogen, phosphorus, and sediment are shown for the two methods for downscaling changes in monthly rainfall volume for the year 2025 and 2050 to hourly rainfall events.
2017 Assessment
Flow
Phosphorus
Nitrogen
Sediment
Equal
decile split
Preferential
decile split
2025
Equal
decile split
Preferential
decile split
2050
Equal
decile split
Preferential
decile split
2025
Equal
decile split
Preferential
decile split
2050
Equal
decile split
Preferential
decile split
2025
Equal
decile split
Preferential
decile split
2050
Equal
decile split
Preferential
decile split
2025
Equal
decile split
Preferential
decile split
2050

## Slide 11
The difference in PET using the Hamon and Hargreaves-Samani methods are shown. For 2025, the Hamon method estimated an increase in PET that was 3.36% greater than that from Hargreaves-Samani method. The change was even more pronounced for 2050, where the Hamon method estimated 6.26 percent additional increase in PET as compared to Hargreaves-Samani. Estimated change in PET using Penman Monteith (short reference) show better alignment with Hargreaves-Samani.
Estimation of potential evapotranspiration (PET)
Percent change in PET
2017 Assessment

## Slide 12
2017 Assessment
Differences in estimated delivery due to methods for estimating potential evapotranspiration for 2025 and 2050 are shown. The differences are higher with increase in temperature.
Flow
Phosphorus
Nitrogen
Sediment
Hargreaves
Samani
Hamon
2025
Hargreaves
Samani
Hamon
2050
Hargreaves
Samani
Hamon
2025
Hargreaves
Samani
Hamon
2050
Hargreaves
Samani
Hamon
2025
Hargreaves
Samani
Hamon
2050
Hargreaves
Samani
Hamon
2025
Hargreaves
Samani
Hamon
2050

## Slide 13
Summary of changes in delivery
Flow
Sediment
Year 2025
Trend rainfall and Ensemble median temperature
Year 2050
Ensemble median rainfall & temperature
Year 2025
Trend rainfall and Ensemble median temperature
Year 2050
Ensemble median rainfall & temperature
Hydrologic response:
rainfall volume & intensity
snow and melt due to temperature
evapotranspiration
Johnson et al. 2003
Bicknell et al. 2005
Sediment response:
rainfall intensity
surface runoff
riverine scour and deposition
2017 Assessment
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs

## Slide 14
Summary of changes in delivery
Nitrogen
Phosphorus
Year 2025
Trend rainfall and Ensemble median temperature
Year 2050
Ensemble median rainfall & temperature
Year 2025
Trend rainfall and Ensemble median temperature
Year 2050
Ensemble median rainfall & temperature
Nitrogen response:
sensitivity to flow
stream bank erosion
denitrification, organic scour
Phosphorus response:
sensitivities to flow and sediment (APLE)
stream bank erosion
scour/deposition of inorganic and organic (HSPF)
Shenk G.
2017 Assessment
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs

## Slide 15
Nitrogen and phosphorus species
Arrows show relatively more increase in organic nitrogen as compared to inorganic.
Arrows show relatively more increase in inorganic (particulate) phosphorus as compared to organic.
2017 Assessment
Year 2025
Trend rainfall and Ensemble median temperature
Year 2050
Ensemble median rainfall & temperature
Year 2025
Trend rainfall and Ensemble median temperature
Year 2050
Ensemble median rainfall & temperature
Simulated changes in nitrogen delivery
Simulated changes in phosphorus delivery
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs

## Slide 16
Uncertainty due to climatic inputs
2017 Assessment
Flow
Phosphorus
Nitrogen
Sediment
Year 2025
Trend rainfall, Ensemble 10%. temperature
Trend rainfall, Ensemble median temperature
Trend rainfall, Ensemble 90%. temperature
Year 2025
Trend rainfall, Ensemble 10%. temperature
Trend rainfall, Ensemble median temperature
Trend rainfall, Ensemble 90%. temperature
Year 2025
Trend rainfall, Ensemble 10%. temperature
Trend rainfall, Ensemble median temperature
Trend rainfall, Ensemble 90%. temperature
Year 2025
Trend rainfall, Ensemble 10%. temperature
Trend rainfall, Ensemble median temperature
Trend rainfall, Ensemble 90%. temperature
Year 2050
Ensemble 10%. rainfall & temperature
Ensemble median rainfall & temperature
Ensemble 90%. rainfall & temperature
Year 2050
Ensemble 10%. rainfall & temperature
Ensemble median rainfall & temperature
Ensemble 90%. rainfall & temperature
Year 2050
Ensemble 10%. rainfall & temperature
Ensemble median rainfall & temperature
Ensemble 90%. rainfall & temperature
Year 2050
Ensemble 10%. rainfall & temperature
Ensemble median rainfall & temperature
Ensemble 90%. rainfall & temperature

## Slide 17
Selections highlighted in yellow are the STAC and CBP climate resiliency workgroup recommendations and CBP approved approaches for the 2017 Climate Change assessment.
For 2035 and 2045 the Modeling Workgroup (September 2018) recommended (a) combining the two sources using weighted means for rainfall, (b) using the ensemble for temperature. Both approaches are consistent with the STAC 2016 Climate Change Workshop recommendations of observed precipitation trends for 2025 and ensemble precipitation estimates for 2050.
Temperature | 
Trend | Ensemble
– | x
? | ?
? | ?
– | x
Precipitation | 
Trend | Ensemble
x | –
? | ?
? | ?
– | x
Year
2025
2035
2045
2050
2019 Assessment

## Slide 18
Flow response
2019 Assessment
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs
Hybrid: weighted average of trend and ensemble
Trend rainfall, Ensemble median temperature
Ensemble median rainfall & temperature
2025
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature
2035
2045
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature

## Slide 19
Sediment response
2019 Assessment
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs
Hybrid: weighted average of trend and ensemble
Trend rainfall, Ensemble median temperature
Ensemble median rainfall & temperature
2025
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature
2035
2045
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature

## Slide 20
Nitrogen response
2019 Assessment
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs
Hybrid: weighted average of trend and ensemble
Trend rainfall, Ensemble median temperature
Ensemble median rainfall & temperature
2025
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature
2035
2045
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature

## Slide 21
2019 Assessment
[1]
[3]
[2]
[4]

## Slide 22
Phosphorus response
2019 Assessment
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs
Hybrid: weighted average of trend and ensemble
Trend rainfall, Ensemble median temperature
Ensemble median rainfall & temperature
2025
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature
2035
2045
Trend rainfall, Ensemble median temperature
Hybrid rainfall, Ensemble temperature
Ensemble median rainfall & temperature

## Slide 23
2019 Assessment
[1]
[2]
[3]
[4]

## Slide 24
Summary and Conclusions
Estimated impacts of 2025 and 2050 climate change on the watershed delivery of nutrients and sediment were shown.
Estimated changes in the delivery of flow, nutrients, and sediment were shown for decadal series of climate change assessments for the years 2025, 2035, and 2045.
Synthesis of inputs and model results provided insights into the overall behavior of the model response.
Analysis did not include changes in land-use, crop yields, atmospheric deposition, and best management practices (BMPs).
Trend-based rainfall projection (estimated from annual data) did not have any monthly/seasonal component.

## Slide 27
Simulated change in export from land
(Phase 6 sensitivities)
Small streams response
(imperviousness + stream bed/bank)
Sparling | Simulation of nutrient species
(nitrate vs. nitrogen)
Riverine response
(scour/deposition + biogeochemical)
Simulated change in hydrology
(HSPF)
Simulated change in sediment washoff
(HSPF)

## Slide 28
Major Basins | PRISM Trend
Youghiogheny River | 2.1%
Patuxent River Basin | 3.3%
Western Shore | 4.1%
Rappahannock River Basin | 3.2%
York River Basin | 2.6%
Eastern Shore | 2.5%
James River Basin | 2.2%
Potomac River Basin | 2.8%
Susquehanna River Basin | 3.7%
Chesapeake Bay Watershed | 3.1%
Change in Rainfall Volume 2021-2030 vs. 1991-2000
[1] Parameter-elevation Relationships on Independent Slopes Model
Rainfall projections using 88-years of annual PRISM[1] data trends
+2.67% (28.10 mm)
+3.14% (34.46 mm)
2017 Assessment
Centre, PA
District of Columbia

## Slide 29
[1] Reclamation, 2013. 'Downscaled CMIP3 and CMIP5 Climate and Hydrology Projections: Release of Downscaled CMIP5 Climate Projections, Comparison with preceding Information, and Summary of User Needs', prepared by the U.S. Department of the Interior, Bureau of Reclamation, Technical Services Center, Denver, Colorado. 47pp.
[1] BCSD – Bias Correction Spatial Disaggregation;
[1] CMIP5 – Coupled Model Intercomparison Project 5
31 member ensemble
An ensemble analysis of statistically downscaled projections were used from BCSD CMIP5[1] dataset.
Change were calculated as differences in 30-year averages.
P90 – 90th percentile
P50 – median ensemble
P10 – 10th percentile
25
0
-25
0 1 2 3
Precipitation Change (%)
Temperature Change (°C)
Ensemble analysis of GCM projections – RCP 4.5
Kyle Hinson, CRC | VIMS
2017 Assessment

## Slide 30
Average annual precipitation and temperature from the 31 bias-corrected downscaled global circulation models are shown for a land segment (N11001). Shown in blue line is the ensemble median. Data used in model calibration from NLDAS-2 are shown in black
Data shown for the District of Columbia for illustration.
2050
2017 Assessment
Temperature
Precipitation

## Slide 31
Summary of RCP4.5 average annual rainfall and temperature change for the Chesapeake Bay watershed are shown. Then range for 10th percentile (P10), ensemble median (P50), and 90th percentile (P90) are shown. The estimated change in rainfall volume based on the extrapolation of long-term trends are also shown (with marker symbol x)
Projected changes in precipitation and temperature (RCP 4.5) – Average Annual
2017 Assessment
extrapolation of trends
Δ 90th percentile (P90)
O Ensemble Median (P50)
10th percentile (P10)

## Slide 32
Monthly change in temperature for the Chesapeake Bay Watershed is shown. Box plot shows distribution of projected change based on 31-member ensemble of RCP 4.5 for the years 2025 and 2050. Additional three marker keys show 10th percentile (P10), ensemble median (P50), and 90th percentile (P90) bounds.
Projected changes in temperature (RCP 4.5)
Watershed average of ensemble median is +2.02 ⁰C
Watershed average of ensemble median is +1.12 ⁰C
2017 Assessment

## Slide 33
Monthly change in precipitation volume for the Chesapeake Bay Watershed is shown. Box plot shows distribution of projected change based on 31-member ensemble of RCP 4.5 for the years 2025 and 2050. For the year 2025 projected change based on long term trend is shown in black line. Additional three marker keys show 10th percentile (P10), ensemble median (P50), and the 90th percentile (P90) bounds.
Projected changes in precipitation (RCP 4.5)
Watershed average of ensemble median is +6.28%
Watershed average of ensemble median is +4.21% (+3.11% estimated using extrapolation of long term trend)
2017 Assessment

## Slide 34
Additional rainfall added to the baseline daily rainfall over the 10-year period for a Phase 6 land segment (Potter, PA) is shown. In the method based on observed intensity trends, (Groisman et al. 2004) more volume is added to 10th decile resulting in higher intensity events become stronger.
Observed changes in rainfall intensity over the last century (based on Figure 10 in Groisman et al. 2004). The equal allocation distribution (blue) is contrasted with the distribution obtained based on observed changes (red).
Monthly delta change to hourly events
2017 Assessment
(Inches)
(Inches)

## Slide 35
Summary of changes in delivery
2017 Assessment
Simulated changes in the delivery of flow, nutrients, and sediment to the Chesapeake Bay for year 2025 and 2050 climate change scenarios are shown.

## Slide 36
2017 Assessment
Trend: projection of extrapolation of long-term trends
Ensemble: 31-member ensemble of RCP4.5 GCMs
Uncertainty due to climatic inputs