## Slide 1: Overview of Climate Impact Assessment Framework and Implementation
Gary Shenk CBPO
STAC Workshop
Chesapeake Bay Program Climate Change Modeling 2.0
9/24/2018

## Slide 2: Accounting for Changing Conditions Cumulative Assessment of Bay Low Dissolved Oxygen Impacts

## Slide 3
GCM Selection Process
Downscaling Method
Observed Trends
Process-based response of flow and sediment
Specified response to flow and sediment
Estuarine Process-based model
Effect on water quality standards
Human responses to climate change
RCP selection
Creation of future climate scenarios
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group

## Slide 4: Chesapeake Bay Program
Modeling for TMDL Water Quality Standards based on 1991-2000 hydrology
Project to 2025 (30 years) and 2050 (55 years)
Presented to Principals’ Staff Committee in 2017. PSC asked for additional analysis to be completed in 2019

## Slide 5
GCM Selection Process
Downscaling Method
Observed Trends
Process-based response of flow and sediment
Specified response to flow and sediment
Estuarine Process-based model
Effect on water quality standards
Human responses to climate change
RCP selection
Creation of future climate scenarios
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group

## Slide 6
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
2016 STAC workshop The Development of Climate Projections for Use in Chesapeake Bay Program Assessments (Johnson et al. 2016).
2025: Use long-term observed trends for precipitation
2050 precipitation and all temperature: Use an ensemble of existing downscaling of CMIP5 models
Carefully consider evapotranspiration
Use RCP 2.6, 4.5, and 8.5
Downscaling Method
Observed Trends
Creation of future climate scenarios
Framework Group

## Slide 7
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Observed Precipitation Trends
1927-2014 PRISM precipitation data
Aggregated to annual values of a county
OLS regression to determine slope
30 years of slope applied to each month of 1991-2000 rainfall data
Downscaling Method
Observed Trends
Creation of future climate scenarios
Framework Group

## Slide 8
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Used RCP 4.5 for scenario run through the full modeling system and shown to PSC
Found significant overlap with RCP 2.6 and 8.5
Downscaling Method
Observed Trends
Creation of future climate scenarios
Framework Group

## Slide 9
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Downscaling Method
Observed Trends
Creation of future climate scenarios
GCM selection
Used the same group of models and model runs that were used in NOAA’s Climate Resilience Toolkit
Precipitation Difference
Framework Group

## Slide 10
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Downscaling methods:
Bias Corrected Spatial Disaggregation (BCSD) - used for runs in 2017
Investigating Multivariate Adaptive Constructed Analogs (MACA)
Investigating Localized Constructed Analogs (LOCA)
Literature exists to support the idea that all are reasonable approaches
Downscaling Method
Observed Trends
Creation of future climate scenarios
Framework Group

## Slide 11
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Downscaling Method
Observed Trends
Creation of future climate scenarios
Ensemble Method
Used the median temperature and precipitation change from the ensemble for each month for the primary run.
Used the corners of the 90th percentile ‘box’ to investigate uncertainty
Precipitation Difference
Framework Group

## Slide 12
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Literature shows that the increases in precipitation over the previous century have primarily occurred in the highest precipitation events.
Downscaling Method
Observed Trends
Creation of future climate scenarios
Two methods of rainfall addition
Multiply all rainfall events by the same factor
Multiply rainfall events within a decile by a factor such that the top decile increases a greater percentage as shown
Framework Group

## Slide 13
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Downscaling Method
Observed Trends
Creation of future climate scenarios
CO2
IPCC 5 Working Group 1
 | RCP 2.6 | RCP 4.5 | RCP 8.5
1995 | 363 | 363 | 363
2025 | 421 | 423 | 432
2050 | 443 | 487 | 541
Framework Group

## Slide 14
GCM Selection Process
Downscaling Method
RCP selection
Watershed Group
Estuarine Group
Downscaling Method
Observed Trends
Creation of future climate scenarios
PET
Use Hargreaves-Samani to calculate change in PET
Function of temperature and extraterrestrial radiation
Apply the change in PET to the Base PET used in the Phase 6 model
Framework Group

## Slide 15
GCM Selection Process
Downscaling Method
Observed Trends
Process-based response of flow and sediment
Specified response to flow and sediment
Estuarine Process-based model
Effect on water quality standards
Human responses to climate change
RCP selection
Creation of future climate scenarios
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group

## Slide 16
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Framework Group

## Slide 17
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Framework Group

## Slide 18
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
HSPF simulation of hydrology is sensitive to:
Precipitation
PET
CO2
Temperature (snowfall and snowmelt)
Framework Group

## Slide 19
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
HSPF simulation of sediment is sensitive to:
Precipitation
Runoff
  PET, temperature, CO2, precip
Framework Group

## Slide 20
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Phase 6 model is time-averaged for N and P from the land
Sensitivity to climate must be specified
Framework Group

## Slide 21
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Nitrogen Sensitivities
Agriculture
  Fertilizer
  Manure
  Atmospheric Deposition
  Fixation
  Crop Cover
  Uptake
Nitrogen Sensitivities
Developed
  Fertilizer
  Atmospheric Deposition
  Crop Cover
  Uptake
Natural
  Atmospheric Deposition
Framework Group
Delivery
  Available water capacity
  Groundwater recharge
  Piedmont carbonate

## Slide 22
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Nitrogen assumption:
  No changes to the concentrations
  proportional change in load to a change in flow.
Phase 5.3.2
  Nitrogen change = 64% of flow change
Framework Group

## Slide 23
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Nitrogen assumption:
  No changes to the concentrations
  proportional change in load to a change in flow.
‘20 watersheds’ study
  Nitrogen change = 115% of flow change
Framework Group

## Slide 24
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Nitrogen assumption:
  No changes to the concentrations
  proportional change in load to a change in flow.
CBPO literature review
  Nitrate change = 100% of flow change
Framework Group

## Slide 25
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
Phosphorus Sensitivities
Agriculture
  Soil P
  Applied Water Extractable P
  Stormflow
  Sediment Washoff
Developed
  Fertilizer
Natural
  Stormflow
  Sediment Washoff
Framework Group
Delivery
  Well-drained soils

## Slide 26
Process-based response of flow and sediment
Specified response to flow and sediment
Watershed Group
Estuarine Group
Creation of future climate scenarios
River Delivery is simulated by HSPF
Scour and deposition of sediment nutrients simulated in rivers greater than 100 cfs
Framework Group

## Slide 27
GCM Selection Process
Downscaling Method
Observed Trends
Process-based response of flow and sediment
Specified response to flow and sediment
Estuarine Process-based model
Effect on water quality standards
Human responses to climate change
RCP selection
Creation of future climate scenarios
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group

## Slide 28
Human responses to climate change
Watershed Group
Estuarine Group
Framework Group

## Slide 29
Watershed Group
Estuarine Group
Nitrogen Sensitivities
Agriculture
  Fertilizer
  Manure
  Atmospheric Deposition
  Fixation
  Crop Cover
  Uptake
Nitrogen Sensitivities
Developed
  Fertilizer
  Atmospheric Deposition
  Crop Cover
  Uptake
Natural
  Atmospheric Deposition
Phosphorus Sensitivities
Agriculture
  Soil P
  Applied Water Extractable P
  Stormflow
  Sediment Washoff
Developed
  Fertilizer
Natural
  Stormflow
  Sediment Washoff
Human responses to climate change
Sensitivities are built in, but need to know how they change in response to human actions
Framework Group

## Slide 30
GCM Selection Process
Downscaling Method
Observed Trends
Process-based response of flow and sediment
Specified response to flow and sediment
Estuarine Process-based model
Effect on water quality standards
Human responses to climate change
RCP selection
Creation of future climate scenarios
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group

## Slide 31
Estuarine Process-based model
Watershed Group
Estuarine Group
CH3D hydrodynamic
CE-QUAL-ICM WQ
  Sediment biogeochemistry
  Sediment Transport
  Living Resources
    SAV
    Oysters
    Menhaden
Framework Group

## Slide 32
Estuarine Process-based model
Watershed Group
Estuarine Group
Framework Group

## Slide 33
Estuarine Process-based model
Watershed Group
Estuarine Group
Considerations
  Sea level Rise
  Surface Temperature
  Ocean Boundary Condition
  Flow, Nutrients, Sediment, Heat from the watershed
Framework Group

## Slide 34
GCM Selection Process
Downscaling Method
Observed Trends
Process-based response of flow and sediment
Specified response to flow and sediment
Estuarine Process-based model
Effect on water quality standards
Human responses to climate change
RCP selection
Creation of future climate scenarios
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group

## Slide 35
Effect on water quality standards
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group

## Slide 36
Effect on water quality standards
Management Effort Adjustment
Watershed Group
Estuarine Group
One regression for each point and each month
Framework Group

## Slide 37: Calculate Climate Effect
Volume Weighted means a ‘red area’ increase of 80 million cubic meters
Effect on water quality standards
Management Effort Adjustment
Watershed Group
Estuarine Group
December 2017 results
Framework Group

## Slide 38: Ran Scenarios with 3% and 6% reduction in Susquehanna N and P
Climate Effect is 9.6% reduction in N and P from the Susquehanna
7.5 Mlbs of N and 0.33 Mlbs of P
The 7.5 million N and .33 million P from the Susquehanna converts to
9.1 million N and 0.49 P Basin-Wide
Effect on water quality standards
Management Effort Adjustment
Watershed Group
Estuarine Group
December 2017 results
Framework Group

## Slide 39: Climate Change Loads: Nitrogen
*Units: millions of pounds
Effect on water quality standards
Management Effort Adjustment
Watershed Group
Estuarine Group
December 2017 results
Framework Group

## Slide 40
GCM Selection Process
Downscaling Method
Observed Trends
Process-based response of flow and sediment
Specified response to flow and sediment
Estuarine Process-based model
Effect on water quality standards
Human responses to climate change
RCP selection
Creation of future climate scenarios
Management Effort Adjustment
Watershed Group
Estuarine Group
Framework Group