## Slide 1
Preliminary Estimates of Future Climate Change Influence On Water Quality In Chesapeake Bay Using CH3D-ICM
Richard Tian, Carl Cerco, Lewis Linker and CBPO Modeling Team
STAC Workshop: Climate Change Modeling 2.0
September 24, 2018
Chesapeake Bay Program
Science, Restoration, Partnership

## Slide 2
Outline
Improved sea level rise simulation
Corrections to air to water heat flux inputs
Updated nutrient loading from the watershed
Refinements to open ocean boundary
Preliminary results

## Slide 3
From Parris et al. (2012). Global Sea Level Rise Scenarios for the United States National Climate Assessment. NOAA Technical Report OAR CPO-1. (1992 used as the starting year)
Following the recommendations of the CBP Climate Resiliency Workgroup, 0.5 m, 0.3 m and 0.17 m of sea level rise were estimated for 2050 moderate, 2025 high, and 2025 moderate, respectively (compared to TMDL baseline of 1995 SL, i.e., mid 1991-2000).
2050: 0.5 m
2025: 0.3 m
2025: 0.17 m
Sea Level Rise Estimates
Linear interpolation and extrapolation for 2035 (0.3 m), 2045 (0.43 m), 2055 (0.57 m) and 2065 (0.7 m).
Climate Resiliency Workgroup will provide best CBP estimates of 2035 and 2045 in 2019.

## Slide 4
Sea level rise simulation
Base
Sea level rise
2.13 m
1.52 m
1.52 m
2.30 m
1.52 m
1.52 m
MSL
Sea level rise
2.13 m
1.52 m
1.52 m
Change the grid
Change the open boundary
Chart: Hypoxia (km3)
| Grid | Boundary
Hypoxia Volume (km3) | 1.53 | 1.53
Hypoxia volume in CB4

## Slide 5
SKY COVER
AIR TEMPERATURE
DEW POINT
WIND
Equilibrium T (TE)
Heat exchange coefficient (KT)
Hex program
T=KE(TE-T)/(Cp•V)
ICM Meteorological Forcing for Heat Transfer From Air to Tidal Waters
Climate Change +Tair(2025) = 1.05 °C
Dew point recomputed assuming relative humidity constant
Relative humidity (RH) remains approximately constant on climatological time scales and planetary space scales (IPCC, 2014)

## Slide 6
Chart: Dischagrge increase (%)
| 2025 | 2050
New | 0.023 | 0.06
Chart: Nitrogen load increase (%)
| 2025 | 2050
New | 0.024 | 0.083
Chart: Phosphorus load increase
| 2025 | 2050
New | 0.031 | 0.153
River discharge
Nitrogen loading
Phosphorus loading
Changes in river discharge and nutrient loading in the 2025 and 2050 climate change scenarios
From Gopal Bhatt

## Slide 7
2050 salinity adjustment at the the ocean open boundary
Constant salinity in vertical profile: +0.4 psu based on Hong and Shen, 2012, supported by Seba et al., 2016 for 2050.
For 2025 0.14 psu (= 0.4 x 0.17/0.5)
Hong and Shen
Seba et al. 2016
0
200
Depth (m)
Hong & Shen 2012
0
25
Depth (m)

## Slide 8
Temperature adjustment at the open boundary
Chart: T (°C)
| 22.3 | 22.07 | 21.92 | 21.8 | 21.71 | 21.46 | 21.31 | 21.3 | 21.3 | 21.3 | 21.3
Base | -1.07 | -2.892 | -4.416 | -5.94 | -7.464 | -8.988 | -10.512 | -12.036 | -13.56 | -15.084 | -16.608
CC2025 | -1.07 | -2.892 | -4.416 | -5.94 | -7.464 | -8.988 | -10.512 | -12.036 | -13.56 | -15.084 | -16.608
Chart: T (°C)
| 14.1 | 14 | 14 | 14 | 14 | 14 | 14.09 | 14.3 | 14.3 | 14.3 | 14.3
Base | -1.07 | -2.892 | -4.416 | -5.94 | -7.464 | -8.988 | -10.512 | -12.036 | -13.56 | -15.084 | -16.608
CC2025 | -1.07 | -2.892 | -4.416 | -5.94 | -7.464 | -8.988 | -10.512 | -12.036 | -13.56 | -15.084 | -16.608
Sep 1, 1993
Nov 15, 1993
Twater=1.0•Tair • Twater/Tsurface
Morrill et al 2014:
An increase in water temperature of about 0.6-1.0°C for every 1°C increase in air temperature.
Twater=0.6•Tair • Twater/Tsurface

## Slide 9
Surface temperature difference between climate change scenarios and the base case, Station CB4.3C.
Erroneous T (°C)

## Slide 10
Chart: T (°C)
| CB2.1 | CB2.2 | CB3.2 | CB3.3C | CB4.1C | CB4.2C | CB4.3C | CB4.4 | CB5.1 | CB5.2 | CB5.3 | CB5.4 | CB5.5 | CB6.2 | CB7.2 | CB7.3 | CB7.4 | CB8.1E
Surface_Summer_2025 | 0.88871 | 0.89687 | 0.87762 | 0.84883 | 0.86089 | 0.90975 | 0.90055 | 0.90153 | 0.89226 | 0.90689 | 0.90112 | 0.91974 | 0.92419 | 0.90961 | 0.87432 | 0.9316 | 0.97156 | 0.96012
Bottom_Summer_2025 | 0.8822 | 0.68617 | 0.76433 | 0.80075 | 0.79393 | 0.81947 | 0.81776 | 0.82577 | 0.8387 | 0.84923 | 0.83625 | 0.91204 | 0.81806 | 0.87209 | 0.92052 | 0.96954 | 0.98023 | 0.90706
Surface_Summer2050 | 1.5698 | 1.6114 | 1.5973 | 1.5102 | 1.52 | 1.5994 | 1.5693 | 1.5895 | 1.562 | 1.5763 | 1.5692 | 1.5798 | 1.5817 | 1.5938 | 1.5257 | 1.6188 | 1.6989 | 1.6602
Bottom_Summer_2050 | 1.5543 | 1.213 | 1.4218 | 1.4373 | 1.4266 | 1.4885 | 1.4849 | 1.496 | 1.5171 | 1.5518 | 1.4439 | 1.6537 | 1.361 | 1.4607 | 1.5879 | 1.6636 | 1.6682 | 1.52
Surface water T change under 2025 and 2050 CC
Thomas et al 2017: data 1982-2014, 0.3 °C per decade;
Preston 2004: Data 1949-2002: 0.185 °C per decade;
Irby et al., 2018: 1.75 °C for 2050.
Bay Mouth
Bay Head
2025 Air T increase 1.05
2050 Air T increase 1.85

## Slide 11
T and T profile at CB4.3C under 2025 CCC
S: surface; b: bottom; m: vertical average over 10 years.
Andrew Sommerlot
0
10
20
30
Depth (m)
T (°C/30yr)
0
2
4
-2
T (°C/30yr)
0
2
4
-2
Summer
Annual

## Slide 12
Chart: Month
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
All10yr_surf | 0.80359 | 0.74741 | 0.85242 | 0.96223 | 0.91546 | 0.866 | 0.88705 | 0.92485 | 0.92431 | 0.87928 | 0.93026 | 0.97704
All10yr_bot | 0.82673 | 0.75881 | 0.84003 | 0.95413 | 0.94363 | 0.78016 | 0.8316 | 0.86201 | 0.79727 | 0.90265 | 0.92345 | 1.0077
Year 2025 CALVERT STMARYS | 0.92394 | 0.91718 | 0.95905 | 1.1767 | 0.96722 | 0.98071 | 1.068 | 1.1407 | 1.159 | 1.0597 | 1.1273 | 1.2195
2025 Air T increase 1.05
2050 Air T increase 1.85
Monthly air T change and surface T simulation at CB4.3C

## Slide 13
Chart: Hypoxia volume (<1 mg/l) in summer (Jun-Sep) 1991-2000 in CB4MH
| Base | 2025 Sea Level Rise | 2025 Flow+Nutrient Loading | 2025 Heat | 2025 All | 2050 Sea Level Rise | 2050 Flow+Nutrient Loading | 2050 Heat | 2050 All | WIP2 | WIP2_2025 | WIP2_2050
 | 1.6107 | 1.5286 | 1.6395 | 1.7314 | 1.6762 | 1.3797 | 1.7122 | 1.8734 | 1.7013 | 0.55679 | 0.61755 | 0.6689
-5%
+1.8%
+7.5%
+4.1%
-14%
+6.3%
+16%
+5.6%
+10%
+20%

## Slide 14
Temperature effects
Dissolved oxygen solubility: a 0.9 °C increase in temperature decreases dissolved oxygen solubility by 0.13 mg/l, or 1.7%.
Biological rates: increase 6% over 0.9 °C (Q10=2)
Stratification (physics)

## Slide 15
Chart: Hypoxia volume (km3)
| Base | Base+DOS | Base+T | Base+Strat.
 | 1.6107 | 1.6708 | 1.6544 | 1.63
+3.7%
+2.7%
+1.2%
Chart: Non-attainment
| Base | Base+DOS | Base+Rate | Base+Strat.
CB4-DC | 0.448 | 0.464 | 0.46 | 0.453
Sensitivity analysis of T modified DO-saturation and biological rate and stratification on water quality, CB4MH, deep channel
DO < 1 mg/l summer 1991-2000
DO non-attainment in CB4 DC
49%
35%
16%
Contribution
Change

## Slide 16
Below Potomac
Transect
CB4/CB5
Transect
CB3/CB4
Transect
CB2/CB3
Transect
6,492 Base
6,854 SLR (6%)
7,235 Base
7,577 SLR (5%)
4,743
5,328 (12%)
5,311
5,891 (11%)
1,908
1,979 (4%)
2,318
2,336 (1%)
782
785
1,356
1,352
Base = Beta 2 Calibration. SLR = 0.5m Sea Level Rise Scenario representing relative Chesapeake sea level riser from 1995 to 2050. Units in mean cubic meters per second (m3/s) for summer 1993 to 1995 hydrodynamics.
Toward Ocean
Toward Head of Bay
Cross-transect water mass fluxes
Base case versus sea level rise (SLR)
Summer 1993-1995

## Slide 17
Estimated DO water quality attainment in the Deep Channel CB4MH under the WIP condition
Chart: Non-attainment
| WIP | WIP_2025 | WIP_2050
DC | 0.0502 | 0.068 | 0.0961

## Slide 18
Temperature is the most sensitive variable in controlling hypoxia under estimated 2025 and 2050 climate change conditions, followed by sea level rise and nutrient loading.
Increased temperature increases hypoxia whereas sea level rise improves DO in the Deep Channel, with the combined effect of an increase in 1.8% non-attainment in CB4 Deep Channel under the WIP condition with estimated 2025 future climate risk.
Sea level rise magnitude: linear interpolation for 2035 and 2045; Waiting for final recommendation from Climate Change Resiliency WG.
Investigation of air to water factor for temperature
at the open ocean boundary ongoing.
Conclusions:
Chesapeake Bay Program
Science, Restoration, Partnership

## Slide 19
Annex

## Slide 20
AR5 global warming increase (°C) projections[7] |  | 
 | 2046–2065 | 2081–2100
Scenario | Mean and | Mean and
 | likely range | likely range
RCP2.6 | 1.0 (0.4 to 1.6) | 1.0 (0.3 to 1.7)
RCP4.5 | 1.4 (0.9 to 2.0) | 1.8 (1.1 to 2.6)
RCP6.0 | 1.3 (0.8 to 1.8) | 2.2 (1.4 to 3.1)
RCP8.5 | 2.0 (1.4 to 2.6) | 3.7 (2.6 to 4.8)
AR5 global mean sea level (m) increase projections[7] |  | 
 | 2046–2065 | 2081–2100
Scenario | Mean and | Mean and
 | likely range | likely range
RCP2.6 | 0.24 (0.17 to 0.32) | 0.40 (0.26 to 0.55)
RCP4.5 | 0.26 (0.19 to 0.33) | 0.47 (0.32 to 0.63)
RCP6.0 | 0.25 (0.18 to 0.32) | 0.48 (0.33 to 0.63)
RCP8.5 | 0.30 (0.22 to 0.38) | 0.63 (0.45 to 0.82)
ICPP AR5 2014

## Slide 22
Below Potomac
Transect
CB4/CB5
Transect
CB3/CB4
Transect
6,483 Base
6,849 SLR (6%)
6,811 SLR NBCC
7,215 Base
7,653 SLR
7,525 SLR NBCC
4,741
5,329 (12%)
5,325
5,296
5,877
5,874
1,919
1,985 (3%)
1,994
2,315
2,328
2,388
Base = Beta 4 TMDL SLR = 0.5m Sea Level Rise Scenario representing relative Chesapeake sea level rise from 1995 to 2050. Units in mean kg DO per second (m3/s) for summer ()Jun-Sept) 1993 to 1995; NBCC: No Boundary Change.
Toward Ocean
Toward Head of Bay
Cross-transect water fluxes (m3/s)
Base case versus sea level rise (0.5m)
Summer 1993-1995

## Slide 23
Surface temperature difference between climate change scenarios and the base case, Station CB4.3C.
Chart: DC non-attainment CB4
| 2017 | 2018
Hypoxia Volume (km3) | 0.4577 | 0.4522
Year
T (°C)
Erroneous T (°C)
m: average over 10 years

## Slide 24
Chart: T (°C)
| CB2.1 | CB2.2 | CB3.2 | CB3.3C | CB4.1C | CB4.2C | CB4.3C | CB4.4 | CB5.1 | CB5.2 | CB5.3 | CB5.4 | CB5.5 | CB6.2 | CB7.2 | CB7.3 | CB7.4 | CB8.1E
Surace_Annual | 0.65096 | 0.72024 | 0.72218 | 0.72737 | 0.75834 | 0.78849 | 0.7832 | 0.78539 | 0.78082 | 0.79067 | 0.78759 | 0.78772 | 0.79026 | 0.76908 | 0.73791 | 0.72093 | 0.68406 | 0.74099
Bottom_Annual | 0.64741 | 0.60555 | 0.70398 | 0.71269 | 0.70123 | 0.71902 | 0.71816 | 0.71506 | 0.71842 | 0.72483 | 0.70112 | 0.73374 | 0.70508 | 0.70662 | 0.64845 | 0.59536 | 0.57261 | 0.58778
Surace_AnnualF1 | 0.78834 | 0.80029 | 0.7514 | 0.74561 | 0.77351 | 0.80248 | 0.7971 | 0.79981 | 0.79617 | 0.80651 | 0.80495 | 0.80864 | 0.81297 | 0.80144 | 0.77739 | 0.81494 | 0.85889 | 0.85076
Bottom_AnnualF1 | 0.78495 | 0.6797 | 0.72673 | 0.75209 | 0.74955 | 0.77382 | 0.77539 | 0.77753 | 0.7856 | 0.7978 | 0.78091 | 0.81958 | 0.78438 | 0.80188 | 0.81006 | 0.8657 | 0.89838 | 0.84942
Changes in surface T simulation by alter open boundary from 0.6 to 1 times of Tair
Open boundary has more influence in deeper layer than in the surface
Chart: Hypoxia (km3)
| F=0.6 | F=1.0
Hypoxia Volume (km3) | 1.63 | 1.64
Hypoxia volume in CB4 under 2025 CC condition

## Slide 25
18 stations along the main stem were analyzed
CB2.1
CB2.2
CB3.2
CB3.3C
CB4.1C
CB4.2C
CB4.3C
CB4.4
CB5.1
CB5.2
CB5.3
CB5.4
CB5.5
CB6.2
CB7.2
CB7.3
CB7.4
CB8.1E

## Slide 26
Chart: DO saturation at 20 psu
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
 | 12.3781 | 12.0568 | 11.7496 | 11.4557 | 11.1744 | 10.905 | 10.6468 | 10.3992 | 10.1617 | 9.9337 | 9.7147 | 9.5043 | 9.3021 | 9.1075 | 8.9201 | 8.7398 | 8.5659 | 8.3983 | 8.2367 | 8.0806 | 7.9299 | 7.7842 | 7.6433 | 7.507 | 7.3749 | 7.247 | 7.123 | 7.0027 | 6.8858 | 6.7723
DO saturation as a function of temperature (Garcia and Gordon, 1992)
0.13
0.9

## Slide 27
Effect of temperature increase on biological rates
ar
ares: Respiration or remineralization rate; B: Biomass;
Tr: Reference temperature; α: rate at reference temperature;
k: Exponential coefficient of temperature effect (0.069; Q10=2)
Irby et al. 2018: Q10=2.1
Londas et al., 2002. Microbial processes and temperature in Chesapeake Bay:

## Slide 28
Chart: Air T at the Patuxent River Station 1985-2017

## Slide 29
Estimate on water quality attainment in the Deep Channel Designated Use

## Slide 30
30
Chart: Resp_ave (g/m3/day)
| Base_average | 2025All_ave | 2025Heat_ave | 2025Flow+Nutrient_ave | 2025SLR17cm_ave
 | 0.28575 | 0.28951 | 0.29334 | 0.28672 | 0.28134
Chart: SOD (g/m2/day)
| Base | 2025 All | 2025 Heat | 2025Flow+Nutrient Loading | 2025 Sea Level Rise
Base 2025 All 2025 Heat 2025Flow+Nutrient Loading 2025 Sea Level Rise | 0.41335 | 0.41199 | 0.40596 | 0.41085 | 0.421
Chart: CL_OW (ug/l)
| Base | 2025 All | 2025 Heat | 2025Flow+Nutrient Loading | 2025 Sea Level Rise
Base 2025 All 2025 Heat 2025Flow+Nutrient Loading 2025 Sea Level Rise | 11.1723 | 11.0971 | 11.1854 | 11.1616 | 11.1516
Chart: GPP (g/m2/day)
| Base | 2025 All | 2025 Heat | 2025Flow+Nutrient Loading | 2025 Sea Level Rise
Base 2025 All 2025 Heat 2025Flow+Nutrient Loading 2025 Sea Level Rise | 1.599 | 1.6606 | 1.64 | 1.6042 | 1.6181
Chart: DO_DC (mg/l)
| Base_DC | 2025All_DC | 2025Heat_DC | 2025Flow+Nutrient_DC | 2025SLR17cm_DC
 | 4.9586 | 4.8179 | 4.7344 | 4.9542 | 5.0487
Diagnosis on Climate Change Scenarios, CB4, average 1991-2000